## Slide 1
SIGNAL PROCESSING PROJECT
Adaptive Irrigation
Management
Through Environmental Condition-Based Water Requirement Estimation
A software-based study of 24-hour-ahead soil-moisture prediction
TEAM MEMBERS
Monica Raghini Chelle • 2520040093 (Team Lead)
Swarna Asritha • 2520040114
Dhanush Karthikeya • 2520040032
GUIDE
Dr. V. Sahiti
Assistant Professor
Department of ECE
KL University, Hyderabad
SOIL SIGNALS → FORECASTS → DECISION SUPPORT
ADAPTIVE IRRIGATION MANAGEMENT
01

## Slide 2
01 • CONTEXT
Introduction & Practical Motivation
02 / 15
WHY SOIL MOISTURE?
• Soil moisture changes as weather, evaporation, rainfall and watering change.
• A forecast 24 hours ahead can help plan irrigation instead of reacting only to current readings.
• Weather-station signals may contain spikes, missing values and rapid changes.
• Signal processing prepares the series; machine learning estimates future moisture.
PROJECT IDEA
01
Observe
Weather + soil data
02
Clean
Hampel filter
03
Predict
LightGBM, +24 h
04
Explain
SHAP + advisory
TAKEAWAY
This project tests whether a signal-processing and ML pipeline improves 24-hour soil-moisture forecasts.
SIGNAL PROCESSING • FINAL PROJECT
02

## Slide 3
02 • PROJECT GOALS
Problem Statement & Objectives
03 / 15
PROBLEM STATEMENT
Noisy and irregular environmental time series can make future soil-moisture prediction difficult. A complex model also needs to be compared fairly with simple baselines.
Research question
Does Hampel cleaning + CEEMDAN analysis + LightGBM improve 24-hour-ahead prediction, and which stages actually help?
PROJECT OBJECTIVES
01
Prepare
Clean, sort and resample station data hourly.
02
Process
Detect spikes with Hampel and analyse components with CEEMDAN.
03
Forecast
Train LightGBM for soil moisture 24 hours ahead.
04
Evaluate
Compare MAE/RMSE with persistence and ridge baselines.
05
Explain
Use SHAP and produce decision-support advice.
TAKEAWAY
The contribution is a tested implementation and honest comparison—not a claim of a new algorithm.
SIGNAL PROCESSING • FINAL PROJECT
03

## Slide 4
03 • RELATED WORK
Literature Review & Research Gap
04 / 15
Ullah et al. (2020)
ANN + Kalman filtering
Sensor-noise reduction in greenhouse environments.
Gap: Different target; no CEEMDAN/SHAP pipeline.
Singh et al. (2019)
ML for smart irrigation
Shows soil moisture can be modelled from IoT data.
Gap: Limited robust filtering and interpretability.
Mabunga & Dela Cruz (2022)
Optimised Gaussian Process
Predicts moisture from environmental variables.
Gap: No multiscale decomposition or SHAP.
Afzal et al. (2025)
ARIMA-based watering
Connects time-series prediction to watering.
Gap: Linear/stationary assumptions; different pipeline.
RESEARCH GAP
We evaluate Hampel + CEEMDAN + LightGBM + SHAP on one real station record and test whether each stage beats simple baselines.
References are listed on the final slide.
SIGNAL PROCESSING • FINAL PROJECT
04

## Slide 5
04 • METHOD
Proposed System: Overview of Our Approach
05 / 15
A software-only pipeline from real station measurements to an interpretable forecast.
01
DATA
Weather-station
records
02
CLEAN
Sort + hourly
resampling
03
FILTER
Hampel spike
replacement
04
ANALYSE
CEEMDAN + IMF
selection
05
MODEL
Features +
LightGBM
06
INTERPRET
Metrics + SHAP
advisory
TARGET
Predict soil moisture (%) 24 hours ahead from current soil and environmental time-series features.
TAKEAWAY
Each stage is evaluated; a more complex pipeline is useful only if the evidence supports it.
SIGNAL PROCESSING • FINAL PROJECT
05

## Slide 6
05 • SYSTEM DESIGN
System Block Diagram
06 / 15
Raw station data
Weather + soil
Preprocessing
Timestamp, gaps,
hourly grid
Hampel filter
Spike detection
and replacement
CEEMDAN
8 IMFs + trend
IMF selection
Retain IMF 7, 8
and trend
Feature building
Lagged + weather
features
LightGBM
Predict moisture
after 24 hours
Evaluation + SHAP
MAE / RMSE / R²
feature explanation
Evaluation is chronological (70% train / 15% validation / 15% test); full-series CEEMDAN has a future-information leakage caveat.
SIGNAL PROCESSING • FINAL PROJECT
06

## Slide 7
06 • DATA
Dataset & Experimental Setup
07 / 15
22,112
raw rows
13,567
hourly values
1,496
Hampel flags
90%
median moisture
DATA SOURCE & TARGET
• P18 BIORO weather-station records (real data).
• Period: 7 Mar 2024 – 13 Oct 2025.
• Target: soil moisture (%) 24 hours ahead.
• Hourly variables include soil moisture, temperature, humidity and rainfall.
CHRONOLOGICAL SPLIT
70%
Train
15%
Validation
15%
Test
Time order is preserved; the last 15% represents about 11 weeks at one station.
TAKEAWAY
The series is often near saturation, so a simple persistence forecast is a strong baseline.
SIGNAL PROCESSING • FINAL PROJECT
07

## Slide 8
07 • SIGNAL CLEANING
Preprocessing: Hampel Filter & Results
08 / 15
WHAT IT DOES
• Compares each sample with a local median.
• Uses median absolute deviation (MAD) as a robust spread estimate.
• Flags points beyond a 3-sigma robust threshold and replaces them with the local median.
• Goal: reduce isolated spikes without heavily smoothing the whole signal.
1,496 points flagged • ~11%
This is relatively high; some real rapid changes may also be removed.
TAKEAWAY
Hampel reduces isolated spikes, but its threshold needs tuning because it flags about 11% of samples.
SIGNAL PROCESSING • FINAL PROJECT
08

## Slide 9
08 • MULTISCALE ANALYSIS
CEEMDAN Decomposition & IMF Selection
09 / 15
WHY CEEMDAN?
• Decomposes a non-stationary signal into oscillatory components (IMFs) plus a residual trend.
• IMFs 1–6 were treated as small, high-frequency components and dropped.
• IMF 7, IMF 8 and the trend were retained for reconstruction/features.
• The residual trend contains about 98% of signal energy.
Important caveat
Full-series decomposition uses future samples; past-only CEEMDAN is the fairer variant.
TAKEAWAY
The trend dominates the signal, and CEEMDAN did not improve the reported baseline metrics.
SIGNAL PROCESSING • FINAL PROJECT
09

## Slide 10
09 • FORECASTING
Feature Engineering & LightGBM Model
10 / 15
INPUT FEATURES
1
Recent history
Lagged soil-moisture observations
2
Signal features
Selected/reconstructed CEEMDAN components and lags
3
Weather context
Temperature, humidity and rainfall-related variables
4
Time context
Hourly time-series alignment
LIGHTGBM REGRESSION
Feature matrix
Past observations
Boosted trees
Learn non-linear patterns
Forecast
Soil moisture at t + 24 h
Training / validation / test split: 70% / 15% / 15% in chronological order.
TAKEAWAY
LightGBM predicts the next-day moisture level from lagged signal and environmental features.
SIGNAL PROCESSING • FINAL PROJECT
10

## Slide 11
10 • RESULTS
Prediction Performance & Baseline Comparison
11 / 15
TEST PERFORMANCE SUMMARY
Test MAE
9.69
Test RMSE
13.90
Test R²
0.785
Train MAE
0.24
Large train–test gap indicates overfitting.
KEY COMPARISON
Best MAE: persistence (5.03)
Best RMSE: LightGBM + Hampel (12.65)
*Full-series CEEMDAN uses future data; its score is not a clean estimate. The report contains slightly different model-summary values across outputs—use the common-split table for baseline comparison.
SIGNAL PROCESSING • FINAL PROJECT
11

## Slide 12
11 • FAILURE MODES
Robustness Testing & Error Analysis
12 / 15
WHAT THE TESTS SHOW
• Injected spikes: Hampel improves LightGBM MAE (9.39 → 7.37 at 10% spikes).
• Random noise: Hampel worsens the reported MAE.
• Large moisture jumps are difficult for both models.
ERROR BY CONDITION
For large jumps (>20 points), model MAE = 36.77 vs persistence = 46.43; on normal hours, persistence is better (2.40 vs 5.10).
TAKEAWAY
Hampel helps with spikes, not all noise; sudden rain/watering changes remain a major error source.
SIGNAL PROCESSING • FINAL PROJECT
12

## Slide 13
12 • INTERPRETABILITY
SHAP Explainability & Irrigation Decision Support
13 / 15
WHAT SHAP ADDS
• SHAP attributes a prediction to contributions from individual features.
• Mean absolute SHAP values rank global feature importance.
• Current soil moisture is the strongest feature in the submitted output.
• The forecast can be passed to configurable rules for an irrigation advisory.
Decision support — not field validated
Rainfall forecasts are not included, limiting anticipation of sudden wetting events.
TAKEAWAY
Explainability highlights current moisture as the dominant driver; recommendations need agronomic validation.
SIGNAL PROCESSING • FINAL PROJECT
13

## Slide 14
13 • WRAP-UP
Conclusion, Limitations & Future Scope
14 / 15
CONCLUSIONS
• Built an end-to-end software pipeline on real station data.
• Hampel reduced spike impact but flagged ~11% of samples.
• Persistence had best MAE; LightGBM + Hampel had best RMSE in the reported common-split comparison.
• CEEMDAN did not improve reported accuracy.
LIMITATIONS
• One station; test period is about 11 weeks.
• Clear train–test performance gap (overfitting).
• No rainfall forecast input.
• Full-series CEEMDAN leaks future information; walk-forward validation remains incomplete.
FUTURE SCOPE
• Use causal/past-only processing and rerun all metrics.
• Tune Hampel threshold and improve IMF selection.
• Add rainfall forecasts and validate across more stations/seasons.
• Reduce overfitting and test with walk-forward validation.
TAKEAWAY
The pipeline is a useful prototype, but current evidence does not show consistent improvement over persistence.
SIGNAL PROCESSING • FINAL PROJECT
14

## Slide 15
14 • ACKNOWLEDGEMENTS
Team Contributions, References & Q&A
15 / 15
TEAM CONTRIBUTIONS
Monica Raghini Chelle
CEEMDAN, IMF selection, past-only variant
Swarna Asritha
Data preparation, Hampel filtering, robustness tests
Dhanush Karthikeya
LightGBM modelling, evaluation, SHAP
SELECTED REFERENCES
• [1] Ullah et al., “ANN Based Learning to Kalman Filter Algorithm for Indoor Environment Prediction in Smart Greenhouse,” IEEE Access, 2020.
• [2] Singh et al., “Machine Learning Based Soil Moisture Prediction for IoT Based Smart Irrigation System,” IEEE SPCC, 2019.
• [3] Mabunga & Dela Cruz, “An Optimized Soil Moisture Prediction Model for Smart Agriculture Using Gaussian Process Regression,” IEEE CSPA, 2022.
• [4] Afzal et al., “IoT-Enabled Adaptive Watering System With ARIMA-Based Soil Moisture Prediction,” IEEE Access, 2025.
• [5] Torres et al., “A Complete Ensemble Empirical Mode Decomposition with Adaptive Noise,” IEEE ICASSP, 2011.
• [6] Ke et al., “LightGBM: A Highly Efficient Gradient Boosting Decision Tree,” NeurIPS, 2017.
• [7] Lundberg & Lee, “A Unified Approach to Interpreting Model Predictions,” NeurIPS, 2017.
THANK YOU
Questions & Discussion
KEY MESSAGE
Evaluate the full pipeline honestly: filtering helps against spikes, but simpler baselines remain highly competitive.
Dataset: P18 BIORO weather-station record, 7 Mar 2024 – 13 Oct 2025. Metrics are from submitted report/output files.
SIGNAL PROCESSING • FINAL PROJECT
15